FOR SALE

Custom Turbocharged 1997 Miata STO (#1138 of 1500)

BEGI Heat-Efficiency Experiment Design  - 317whp/284ftlb

$15,000

ENGINE

Race-Prepped Block

  - 1.5mm over bore Wiseco forged pistons  (2.0L final displacement)

  - '99 head, ported and port-matched

  - 1mm oversized, waisted, backcut, multi-angle, black-nitrated valves

  - knife-edged, lightened crank

  - crank, pressure-plate, and fly-wheel balanced as a single unit

Custom long-runner intake manifold, w/ 92mm throttle-body  (30mm over stock)

Coil-on-Plug (COP) ignition (300% spark capacity over stock)

Mechanical and electric water-pumps; 1 for each cooling path w/ independent thermostats

Dual-radiators w/ 143% frontal surface area over stock, w/ twin SPAL high-flow fans

225-lpm fuel pump				Oil-cooler w/ thermostat

Remote, oversized oil-filter			Adjustable Timing Gears

TURBO

Garrett T03/04-46E Turbo				Tial External Adjustable Wastegate

High-Mount Air-to-Air intercooler			Oil & Coolant Heat-Sink

Compact dual ceramic catalytic converters  (1-lb of back pressure at WoT)

SAFETY

Flyin' Miata “Big Brake” Kit, w/ slotted front & rear rotors and Wilwood front calipers

Hard Dog Hardcore (Hardtop) Roll Bar		Willans 6-point harnesses (Driver & Passenger)

Stainless brake lines				Street/Track composition pads front & rear

Competition-grade hoodpins			Anti-Submarine Brace for Driver  (currently not installed)

ADDITIONAL FEATURES

MS-PnP (v1) ECU w/ Dyno-Tuned engine mapping  (and laptop w/ software)

3.63:1 TORSEN Type-II Limited Slip Rear-End

ACT Stage-II Clutch				Stainless Clutch line

Mazda Competition Motor Mounts			Mazda Competition Transmission Mounts

Mazda Competition Rear-Diff Mounts

KYB AGX 8-way adjustable shocks		Flyin' Miata Rear Shock Mounts

Flyin' Miata (Lowering) Spring Set			Flyin' Miata Front & Rear Heavy-Duty swaybars

Racing Beat adjustable heavy duty end links	Racing Beat Front Lower Control Arm Brace

Racing Beat Heavy-Duty (reinforced) Front Sway-Bar mounts

Racing Beat Front and Rear Swaybar bushings

Passive under carriage air-ducting w/ rear diffuser

Intake & exhaust venting, providing fresh air feeds to all heat exchangers

Modified “Lanny Chambers” alignment

16in Enkei RP-F1 lightweight rims			205/45-R16 Bridgestone Potenza 760 Sport Tires

Functional Air Conditioning			Kenwood AM/FM/CD w/ door & headrest speakers

Leather interior					Hardtop

New soft top (not installed)			Various spare parts

Contact Larry via eMail  [  lrbader@att.net ]